## Slide 1: Media and Event production via Resilient Communication on IoT Infrastructure
Overview
19th of April 2024

## Slide 2: Agenda
  MERCI project overview
  Some Use-Cases
  Some Highlights (so far)
  Takeaways

## Slide 3: About MERCI
German-Franco innovation project for private 5G networks
  The only one not using 3GPP technologies
Funded by the Bundesministerium für Wirtschaft und Klimaschutz (BMWK) and the französischen Ministère de l’Economie et des Finances et de la Relance (MEFR) (via BPI)
Media and Event production via Resilient Communication on IoT Infrastructure
Develop innovative solutions based on the non-cellular 5G technology DECT NR+ for private networks through cooperative integration of
  the media & event sector, manufacturing/producing content up to distribution to the audience,
  with the (industrial) IoT sector,

## Slide 4: About MERCI
MERCI has three main goals:
Integration of DECT NR+ in existing wireless communication infrastructures
Evaluation and demonstration of the DECT NR+ technology and their possibilities
Practical evaluation of new frequency bands for private 5G networks
Enabling 5G for small and medium enterprises via non-cellular DECT NR+
Increase the European sovereignty on wireless communication technology and eco-systems
Partners
Associated Partners
more to come…

## Slide 5: MERCI Work Packages

## Slide 6: MERCI Consortium
Event & Media Production
(Industrial)
Internet of Things
Audio
Video
Audience
IoT Cluster
URLLC IoT
Massive IoT
Meshed Audio, SDR Implementations
Integration/Monitoring
Spectrum
Sharing

## Slide 7: Timeline
MERCI End 04/2025
MERCI Start 11/2022
30 months
Use-Cases & Requirements
Component Development
Evaluation & Demonstration
Integration
MERCI Public Workshop
MERCI Final Workshop
early outcomes

## Slide 8: DECT NR+
Straight forward innovation path for many existing use cases
  Evolving the advantages of DECT into the 5G world
  Open Standardization by ETSI
  Access to additional IMT and non-IMT frequency bands
Technology enablers for known and new uses
  New flexible PHY/MAC engine based on OFDM TDMA/FDMA
  URLLC and mMTC feature support beyond IMT-2020 vision and requirements
  New network topologies (Point-to-Point, Star, Mesh Tree)
  Designed for operation below 6 GHz, including 1.9 GHz
  Support of different medium access principles (e.g., Listen Before Talk, Schedules Access).
Convergence
E2E security
DLC
MAC
PHY
Pro Audio

## Slide 9: DECT NR+ in various environments
Model | Indoor NLOS Thick concrete walls | Urban Micro NLOS Urban no line of sight | Urban Micro LOS Urban line of sight | Urban Macro LOS Line of sight over rooftops
Environment | Basement, metering room | Urban Area | Rural Area | Unrealistic use-case
Range | 80m | 320m | 1700m | 7000m
Same DECT NR+ radio in all models (*)
* actual measurements: 650m Urban Micro LOS; 6500m Urban Macro LOS by MERCI partner Wirepas

## Slide 10: Use Cases Overview
Feasibility and Performance - Generic Benchmark Use cases
  Baseline Operations
  Coexistence
  Spectrum Management
  Interworking with different Network and Technology
Industry Oriented Solutions
  Video Camera Robot, Cooperative Transport of Goods
IoT Oriented Solutions
  Utilities Service Scenarios, Industry and Building Monitoring/Sensor use
Media Oriented Solutions
  A4V, Music Industry, Conferences, Mic/Loudspeaker Systems, Mesh AV Production, AGV-enabled Camera/Mic Tracking

## Slide 11: Some Use Cases - Media
DECT-2020 NR for the communication in wireless acoustic sensor networks (WASNs) and object audio distribution
DECT-2020 NR for the communication in wireless acoustic sensor networks (WASNs) and object audio distribution
DECT-2020 NR for the communication in wireless multi-loudspeaker systems received as MPEG-H object audio
Handheld camera in a Venue
AGV-enabled camera-/microphone tracking
Notes: Ateme 3

## Slide 12: Some Use Cases – Spectrum & Interoperability
Managed spectrum access for temporary usage
DECT 2020 as 3GPP RAN network enabling non-3GPP access
DECT-2020 FT acts as an internet route via 3GPP connection
Notes: Ateme 4

## Slide 13: Some Use Cases - Industry
Robot with video camera in a factory
Cooperative Transport of Goods
Notes: Vitec 3

## Slide 14: Some Use Cases - IoT
Smart Metering
    Industry and building monitoring/sensor use
Building automation use case examples:
Climate control, including temperature, humidity, vibration, etc.
CO monitoring
Electrical usage
Fire detection
Heating, ventilation, and air conditioning systems (HVAC)
Lighting control
Occupancy
Security and access control
Structural health
Water monitoring
Collection and analysis of real-time data from sensors and equipment’s enables
to Improve building energy efficiency, it can
reduce maintenance costs with predictive maintenance.
Applications to optimize space utilization, such as office desk and seat occupancy information
DECT2020 NR enables simple large scale (distance and number) reporting and management
Notes: Wirepas 2

## Slide 15: Spectrum Access and Management
Spectrum Repository
  Available frequency bands and access rules
Device capabilities
  Supported bands
  Simultaneous Joint Operation, e.g.
    Control & Audio in DECT band
    Video in 3.8-4.2 MHz
Options
  Independent Network at A
  Independent Network at B
  Network B anchored in Network A, or vice versa
How to organize?
A: 1880 – 1900 MHz
B: 3800 – 4200 MHz
Example: 3.8-4.2 GHz link anchored in DECT band

## Slide 16: Highlights - early outcomes
Deliverables progressing well.
R&D Eco-System starting to develop.
Hardware:
  nRF9161 evaluation boards up and running.
  USRP SDR implementation of PHY and some MAC functionalities focused on scheduled access.
Demos:
  First Audio transmission via DECT NR+ demonstrated (RFmondial/LUH)
    streaming audio transmission over DECT NR+ based on Nordic Chipset and SDR implementation (interworking) with simultaneously running spectrum scanner (Nordic chipset)
  5G Mesh IoT Demo (Wirepas)

## Slide 17: First PCB (10/2023)
Dimensions: 10 cm × 5 cm
NRF9160 or NRF9161 with DECT NR+ modem
Host processor running embedded Linux
Interfaces
  Two analog audio inputs + two outputs
  Gigabit Ethernet
Current DECT NR+ firmware
  Audio encoding on host
  NRF916x low latency scheduled access

## Slide 18: Highlights

## Slide 19
Head-End
System
Test environment built in Wirepas to emulate a Smart Metering deployment
200 nodes
1 Gateway
Cloud connectivity
Wirepas Network Tool
DECT NR+ IoT Mesh
Notes: To conclude on smart metering, with 5G Mesh, deployments…

## Slide 20: MPEG-H 3D Audio in the context of MERCI
Mix
Encoding
Packaging/Mux
Restitution
Authoring
Pre-processing
Uncompressed audio
+ metadata
Audio source
Audio source
Audio source
Audio source
Audio source
Audio source
DECT 2020 NR
German commentary
French commentary
5.1 audio bed
ST2110
DECT 2020 NR
Achieved so far
ST2110 dynamic metadata (S-ADM) support
Live MPEG-H 3D encoding with dynamic configuration changes (metadata-driven)
DASH and HLS fMP4 packaging with high- and low-level signalization

## Slide 21: Ultra Low Latency (ULL) video suitable for DECT NR+
Video Source
VITEC PICO+ Video encoder
1 GbE LAN
PC with ULL VLC playback
VITEC ACE Video Decoder
HW decoding delay
SW decoding delay
  Latency observed : 50 ms for HW decode, 380 ms for SW decode

## Slide 22: Takeaways
DECT NR+ is a non cellular standard developed by small and medium European companies
  Available chipsets optimized to targeted applications: simple and cost efficient
First result confirm enabling by DECT NR+ of new applications
  Development ongoing show that DECT NR+ is well suited for the targeted applications
  First performance evaluations
  Already some results fed into the standard (DECT-2020 NR) for fixes and enhancements
  More to come with (full) end to end demonstrators and further evaluations
MERCI’s Unique Approach - Potential example to follow in future on how to „fuel“ standards deployment/development?
  Complete different industry sectors gather to evaluate, verify and develop the ecosystem to complement a technology standard

## Slide 23: Questions?