## Slide 1: Harmonizing the Spectrum: Insights into the 3.8 – 4.2 GHz Band and Private Network Implementation
Prof. Dr. M. Dolores Pérez Guirao, Argianto Rahartomo
Ostfalia Hochschule für Angewandte Wissenschaften
(Ostfalia University of Applied Sciences)
{m.perez, a.rahartomo}@ostfalia.de

## Slide 2: Agenda
DECT-2020 NR short introduction
Private Network & Spectrum Access
The European Harmonized 3.8 – 4.2 GHz Frequency Band
Use Cases
Spectrum Sharing
  Introduction
  Brief history
  MERCI viewpoint
Spectrum Sharing in MERCI
  ETSI Working Document (Studies on Information Elements)
  Ostfalia Spectrum Access for temporary usage Architecture
Future Work
Partners
Associated Partners
more to come…

## Slide 3: DECT-2020 NR short introduction
Question:
What is the benefit of non-cellular 5G?
DECT-2020 NR, developed by ETSI, is a Radio Interface Technology (RIT) that aligns with ITU-R’s
IMT-2020 requirements as part of the 5G standard
DECT-2020 NR is the first non cellular 5G Technology standard
Answer:
To facilitate private networks that might benefit vertical industries, including small and medium enterprises.
Vertical Industries including Programme Making and Special Event Industries, Wireless Industrial Automation, and Utilities
Fig.1 ITU R Press Release
Fig.2 DECT-2020 NR fulfills two 5G requirements

## Slide 4: Private Network & Spectrum Access
Technology
Spectrum
Business
Q: What should be considered?
Typical Question:
Are the equipment available?
Can the industry achieve economic scale benefits?
Is my equipment capable of operating across borders?
Typical Question:
Which Spectrum is available?
Is it available at regional, national, or global levels?
e.g., 3GPP, DECT
Option to access spectrum for the Private Network:
Local license directly from the regulator
Having contract an MNO
Lease spectrum from Incumbent
Spectrum Sharing
Fig.3 Level/Condition to deploy private network
Notes: Local license directly from the regulator -> National-level only
Having contract with the Incumbent -> Not an interesting option for the vertical industry due to reliability, data privacy, etc.
Lease spectrum from Incumbent -> Basically same with point 2
Spectrum Sharing

## Slide 5: The European Harmonized 3.8 – 4.2 GHz Frequency Band (1): Introduction
European (through EC) recommends its member states to consider shared use of 3.8 – 4.2 GHz frequency band for local applications using Low/Medium Power Networks due to existence of incumbent applications and services
This band supports 5G equipment, but the band is not dedicated to MNOs in Europe
The local band must be shared by considering:
  Incumbent Protection within the band
  Need for coordination of local area networks in the band
  Adjacent coexistence with adjacent services, mainly MNOs below 3.8 GHz

## Slide 6: The European Harmonized 3.8 – 4.2 GHz Frequency Band (2): Operating Frequency Band
DECT-2020 NR (or DECT NR+ terms which are promoted by DECT Forum) has access to the DECT Core Band (License-Exempt 1.9 GHz)
Band number | Receiving band (MHz) | Transmitting band (MHz)
1 | 1 880 to 1 900 | 1 880 to 1 900
2 | 1 900 to 1 920 | 1 900 to 1 920
3 | 2 400 to 2 483,5 | 2 400 to 2 483,5
4 | 902 to 928 | 902 to 928
5 | 450 to 470 | 450 to 470
6 | 698 to 806 | 698 to 806
7 | 716 to 728 | 716 to 728
8 | 1 432 to 1 517 | 1 432 to 1 517
9 | 1 910 to 1 930 | 1 910 to 1 930
10 | 2 010 to 2 025 | 2 010 to 2 025
11 | 2 300 to 2 400 | 2 300 to 2 400
12 | 2 500 to 2 620 | 2 500 to 2 620
13 | 3 300 to 3 400 | 3 300 to 3 400
14 | 3 400 to 3 600 | 3 400 to 3 600
15 | 3 600 to 3 700 | 3 600 to 3 700
16 | 4 800 to 4 990 | 4 800 to 4 990
17 | 5 725 to 5 875 | 5 725 to 5 875
18 | 5 150 to 5 350 | 5 150 to 5 350
19 | 5 470 to 5 725 | 5 470 to 5 725
20 | 3 800 to 4 200 | 3 800 to 4 200
21 | 3 700 to 3 800 | 3 700 to 3 800
DECT Core Band
Our project would like to investigate this band
Tab.1 Operating Frequency Band Table

## Slide 7: The European Harmonized 3.8 – 4.2 GHz Frequency Band (3): Workflow Interaction
Fig.4 Workflow interaction between European policy making bodies to harmonize the band

## Slide 8: Two samples of Use Cases
#2 DECT 2020 NR in IMT Bands with IoT Control Channel
#1 Managed Spectrum Access for Temporary Usage
Q: How these use cases can be realized?
Fig.6 IoT Control Channel use case
Fig.5 Managed Spectrum Access use case

## Slide 9: Spectrum Sharing (1): Introduction
Regulation Perspective
Technical Perspective
“A condition where users reuse radio waves across dimension space, frequency, time, and signal domain (code)” (Pandit and Singh, 2015)
“It refers to the situation where two or more radio systems use the same frequency band” (ITU-R, 2014)
Spectrum Sharing
Sensing
Coordinating
Informing
always apply at least one of these*
Spectrum Sharing
Horizontal
Vertical
There are two types:
*Currently, the application of AI is under investigation
Notes: AI approach also currently being investigated
SU between SU
PU and SU in Horizontal spectrum sharing
AI approach also currently being investigated
S. Pandit and G. Singh, “An overview of spectrum sharing techniques in cognitive radio communication system,” Wireless Networks, vol. 23, no. 2, pp. 497–518, Feb. 2017, doi: 10.1007/s11276-015-1171-1.
https://www.itu.int/dms_pub/itu-r/opb/rep/R-REP-M.2330-2014-PDF-E.pdf
Radio Engineers work for the past over years to develop automated technologies that allow different radio systems to share frequencies in an automatic or dynamic way
Icon chip manufaturer source: https://cdn-icons-png.flaticon.com/512/165/165325.png
Icon European Regulator source: https://www.flaticon.com/free-icon/regulation_8146907
The regulation is not clearly stated mandatory of using spectrum database nor automated coordination, our project assumes using spectrum database nor automated coordination are used
We do not to what extend it can go
What is the meaning this band is important?
eLSA/DSAS problem: They meet in frequency agnostic, no regulation decision
Potential New use cases
Handshaking: Equipment (Chip manufacturers want to create if the market demands) and Regulation
EU not really discuss about Automated Coordination regulation, only the technical

## Slide 10: Spectrum Sharing (1): Introduction
Regulation Perspective
Technical Perspective
Typical Questions are:
Who holds the rights to the spectrum?
Which users are entitled to these rights?
Under what conditions can these rights be granted?
Typical Questions are:
How can regulation be enforced?
How can sharing be made more efficient?
Sharing Scheme:
Incumbent protection from being interfered by secondary users
To coordinate secondary users among themselves
Q: Why do we need Spectrum Access/Sharing?
A: Increasing demand for local private wireless networks
It refers to a connectivity which controlled and managed by private organization and
A high level of Quality of Service
Notes: AI approach also currently being investigated
SU between SU
PU and SU in Horizontal spectrum sharing
AI approach also currently being investigated
S. Pandit and G. Singh, “An overview of spectrum sharing techniques in cognitive radio communication system,” Wireless Networks, vol. 23, no. 2, pp. 497–518, Feb. 2017, doi: 10.1007/s11276-015-1171-1.
https://www.itu.int/dms_pub/itu-r/opb/rep/R-REP-M.2330-2014-PDF-E.pdf
Radio Engineers work for the past over years to develop automated technologies that allow different radio systems to share frequencies in an automatic or dynamic way
Icon chip manufaturer source: https://cdn-icons-png.flaticon.com/512/165/165325.png
Icon European Regulator source: https://www.flaticon.com/free-icon/regulation_8146907
The regulation is not clearly stated mandatory of using spectrum database nor automated coordination, our project assumes using spectrum database nor automated coordination are used
We do not to what extend it can go
What is the meaning this band is important?
eLSA/DSAS problem: They meet in frequency agnostic, no regulation decision
Potential New use cases
Handshaking: Equipment (Chip manufacturers want to create if the market demands) and Regulation
EU not really discuss about Automated Coordination regulation, only the technical

## Slide 11: Spectrum Sharing (2): Brief History of Spectrum Sharing
2023
05
2015 - 2017
04
2011 - 2013
03
2010
02
Early
2000s - 2009
01
Television White Space (TVWS) was defined.
No guaranteeing for QoS
The advent of Cognitive Radio & FCC warned about a looming spectrum crisis (Spectrum Crunch)
Nokia and Qualcomm introduced the concept of Authorized Shared Access (ASA) and RSPG formally described the concept of Licensed Shared Access (LSA)
Dynamic Spectrum Allocation Service (DSAS) System Requirements (ETSI TS 104 011) was published
CBRS was created and initialized
eLSA was technically specified
Notes: LSA was the first spectrum sharing approach that targeted QoS service guarantees for non primary users, in this case ’licensees’ [19], which can be viewed as an important breakthrough to make spectrum sharing commercially viable.
But it is not local, it is national level which is only for long term and cover entire nation.

## Slide 12: Spectrum Sharing (3): MERCI viewpoint on Spectrum Sharing
Spectrum Sharing
Technical
Regulation
I want to create chip for the equipment if the market demands it.
Chip Manufacturer
We do not enforce “Spectrum database” or “Automated coordination” yet
Europe Policy making bodies
One of our objectives in MERCI project is to investigate the use of Spectrum Database and Automated Coordination concepts to scale-up the deployment of private networks, drawing on the commercial achievements of CBRS and AFC in the US market.
Notes: Icon chip manufaturer source: https://cdn-icons-png.flaticon.com/512/165/165325.png
Icon European Regulator source: https://www.flaticon.com/free-icon/regulation_8146907

## Slide 13: Spectrum Sharing in MERCI
ETSI TC DECT
Testbed Implementation Work
Licensed spectrum access requires the applicant to obtain a license from a competent regulatory authority or in some cases a designated band manager or spectrum database manager (spectrum controller)
We make, as a first step, Cloud-based Spectrum Access which accommodate local licensing in certain geographical area within specified time frame
We have this local network, and layer of coordination and we believe it can have better scalability, accessing spectrum in a more efficient way than non automated approach
We will show our system interface and architecture
We investigate current DECT-2020 NR standards and look if everything is considered
There are two working documents we are considering:
  Considering the first use case, is getting a local license for temporary usage e.g., PMSE
  Considering the second use case, is getting a local license from parallel band & cooperation

## Slide 14: ETSI Working Documents on Information Elements
Study on Information Elements
ETSI DECT TR
A Study on Information Elements for
Network Cooperation: Advertising
Cooperation offer or need for
Cooperation
ETSI DECT TR 104 046
A Study on Information Elements and
Functionalities for Spectrum
Management including provisioning
Of channel usage information

## Slide 15: Ostfalia Spectrum Access for temporary usage System Architecture
Notes: Establish temporary network with local license (green), other colors are obtained from regulation restriction.
Working on concept through the license and can enforce the transmitter so the equipment follows

## Slide 16: Future Work
Advancements in electronic Key for enhancing trust
Broadening the scope of the demonstrator to include not only temporary usage but also coordination among Secondary Users
Progressing work on two technical reports