## Slide 1: Video via DECT NR+ MERCI Public Workshop Hannover, April 19
Eric DENIAU Maxim PENNER

## Slide 2: Use Cases Considered
Media production use case : Handheld camera in a Venue
Industrial use case :
Robot with video camera in a factory

## Slide 3: Video transmission Challenges
Encoder efficiency & compacity
  High compression rate
  Embedded encoding & decoding
“glass to glass” video latency
  Below human perception
Wireless transmission
  Lowest interference
  Highest range

## Slide 4: Demo set-up
PICO+ Video encoder
PC with ULL SW playback
VITEC ACE Video Decoder
Hardware decoding delay
Software decoding delay
Diamond-H Video encoder
HDMI
SDI
Video Source
DECT NR+

## Slide 5: Why DECT NR+ is suitable for wireless video streaming
Low latency enabled by
  Flexible numerology allowing very short symbols
  Flexible channel coding with short code blocks
  No infrastructure implies no infrastructure delays
Transmission reliability enabled by
  CP-OFDM adaptable to different wireless environments
  HARQ
  Robust antenna configurations with up to eight antennas
  Large variety of usable frequency bands (IMT, DECT)

## Slide 6: Video transmission with the NRF9161
NRF9161 is accompanied by host system running Linux
Host can
  Encode/decode analogue audio and transmit/receive via DECT NR+
  Forward external application data via DECT NR+ (this demo)
NRF9161 is fully configured from host
Video transmission parameters
  16-QAM
  Packet length 1.7ms
  Packet rate > 200 Packets/s
  Data rate > 1Mbit/s