## Slide 1: AMR use case with DECT NR+
Wirepas
5G Mesh demo for smart metering

## Slide 2: Wirepas AMR reference: Complete meter and gateway integration
Software: Provide a first level of integration of key functionalities tuned for Wirepas 5G Mesh in order to maximize the technology benefits
  NIC: Pre-integration of DLMS Client and associated and tested against selected meter. It includes FOTA for Smart Meter, Clocks, IPV6 …
  Gateway: IPV6 and Smart Metering specific component
  Backend: Integration guidelines and WNT used as NMS.
Hardware: Provide an optimized SW design database of a System on Module (SOM) to be used by integrator to build NIC Card.

## Slide 3
This small mesh network operation:
integrates assets based on NR+ standard on existing commercial HW
shows basic NR+ features such as adaptive transmit power and frequency hopping
Hardware: Nordic Semiconductor nRF9161 based Thingy:91X
Firmware:
  demo application
  Wirepas 5G protocol stack
  Nordic NR+ modem PHY/L1 FW
Band: 1881 – 1899 MHz
TX power: +19 dBm max.
Wirepas 5G Mesh 1.9 GHz Demo
Demo Application
  Wirepas 5G protocol stack
  Nordic NR+ modem PHY/L1 FW
Device Hardware

## Slide 4
WNT Backend
AWS Cloud
PC
WNT Client
Internet
Thingy:91X
USB-C
4G Access Point
LAN
Grafana
LAN
running Nordic NR+ modem L1/PHY + Wirepas 5G Mesh protocol stack + dualmcu_app
  running Nordic DECT2020 NR+ modem L1/PHY + Wirepas 5G Mesh protocol stack + demo application
Demo components

## Slide 5: Wirepas DLMS Integration package Software
NIC Application
DLMS Application reference including DLMS Client and Server
Scheduled meter reading and conversion from Push to Pull
DLMS Pass Through
Key Handling
OTAP
IPV6 UDP
UART and SPI drivers
Gateway
Wirepas Gateway Drivers
IPV6 or MQTT support
Dual transport for HES and NMS connection
Backend
Wirepas Network Tool (NMS)
IPV6 or MQTT support
Examples for HES integration
Benefits for the integrator:
Provide an almost complete baseline from NIC to Cloud to ease integration and ensure optimal performances at scale.
Accelerate time to market
Integrator accountabilities
Final integration and testing against deployed smart meters.
Potential adaptations upon specific tender requirements
Gateway integration:
  Gateway Device management (Update, OS management, networking)
  Software porting on selected hardware
  Backhaul integration and management (ie: cellular)
HES / MDM integration

## Slide 6: Wirepas AMR Reference at a glance
Objectives
Provide System integrators a comprehensive kickstart package for their AMR system development
Accelerate, simplify and raise overall system performance at scale
Wirepas AMR Reference is a solid and quite complete starting points
RF Mesh integration in meter and HES in NO TIME thanks to :
Compliancy with DLMS allowing simpler HES integration

## Slide 7: Seamless radio selection between SubGHz and 5G Mesh
One Application, many meters, 2 RF profiles
Tested against multiple meter manufacturers
One code: SubGHz and 5G Mesh

## Slide 8: Wirepas NMS: Complete solution for network monitoring and device management
Manages millions of meters
Support SBD requirements
Complete API for HES integration
Built in advanced alerting
Support OTAP including smart meter optimized OTAP